## Slide 1: MEE427 Microcontroller Overview
29/02/2024

## Slide 2: PIC 16F877A

## Slide 3: Components and Software
Needed Hardware;
  PIC 16F877A
  PIC Programmer (available)
  Crystal and capacitors
  Max232 and rs232 to usb converter or FTDI Cable or Arduino Uno without chip (needed for debugging)

## Slide 4: What needed as Hardware
PIC16F877A
40 Pin Socket
Crystal 20MHz
22 pF Capacitor (x2)
Perforated Board
40 pin male header
10kΩ Potentiometer
1 Tach Button
10k Resistor
Fuse (2A) and Fuse Socket
7805 5V Regulator
Terminal Blocks (x8)
PIC Programmer (Available)

## Slide 5: Connections
Reset pin should be powered
OSC1 & OSC2 should be connected to crystal and 22pF capacitors
Programmer is connected to Reset, PGD & PGC pins.

## Slide 6: Hardware
Minimum connection for PIC16F877A

## Slide 7: Proper PIC16F877A Custom Board
Advantages;
  Strong connections
  Proper code uploading opportunity (less damage)
  Customization possibility

## Slide 10: Components and Software
Needed Software
CCS C Compiler (Coding Environment and Converter to .hex)
Proteus (Simulation Environment)
PIC Programmer Software
  MPLAB X IPE
  PICkit™ 3 Programming App and Scripting Tool